## Slide 1
Dr. Asif Zaman
Associate Professor, CSE, RU
CSE3151
Computer Networks
(Session 2018-19)

## Slide 2: From Syllabus
Medium Access Sublayer

## Slide 3
Network links can be divided into two categories:
  those using point-to-point connections and
  those using broadcast channels. Also called: multi-access channels or random access channels

## Slide 4: MAC (Medium Access Control)
The protocols used to determine who goes next on a multi-access channel belong to a sublayer of the data link layer called the MAC (Medium Access Control) sublayer.
The MAC sublayer is especially important in LANs, particularly wireless ones because wireless is naturally a broadcast channel.

## Slide 5: The Channel Allocation Problem
Two Schemes:
Static Channel Allocation
dynamic channel allocation
X
A
B
C

## Slide 6: Static Channel Allocation
FDM (Frequency Division Multiplexing).
User needed to be constant N
When some users are quiescent, their bandwidth is simply lost.
A static allocation is a poor fit to most computer systems… peak traffic to mean traffic ratios of 1000:1
Most of the channels will be idle most of the time

## Slide 7: Dynamic Channel Allocation
Assumptions:
  Independent Traffic.:
    The model consists of independent stations ….
    The expected number of frames generated in an interval of length , where λ is a constant (the arrival rate of new frames).
    Once a frame has been generated, the station is blocked and does nothing until the frame has been successfully transmitted

## Slide 8: Dynamic Channel Allocation
  Single Channel.
    A single channel is available for all communication.
    All stations can transmit on it and all can receive from it.
  Observable Collisions.
    If two frames are transmitted simultaneously, they overlap in time and the resulting signal is garbled.
    This event is called a collision.
    All stations can detect that a collision has occurred.
    A collided frame must be transmitted again later. No errors other than those generated by collisions occur

## Slide 9: Dynamic Channel Allocation
  Continuous or Slotted Time.
    Time may be assumed continuous, in which case frame transmission can begin at any instant.
    Alternatively, time may be slotted or divided into discrete intervals (called slots).
    Frame transmissions must then begin at the start of a slot.
    A slot may contain 0, 1, or more frames, corresponding to an idle slot, a successful transmission, or a collision, respectively.

## Slide 10: Dynamic Channel Allocation
  Carrier Sense or No Carrier Sense.
    With the carrier sense assumption, stations can tell if the channel is in use before trying to use it.
    No station will attempt to use the channel while it is sensed as busy.
    If there is no carrier sense, stations cannot sense the channel before trying to use it.
    They just go ahead and transmit.
    Only later can they determine whether the transmission was successful

## Slide 11: Multiple Access Protocols
Popular Dynamic Channel Allocation Protocol:
  ALOHA
    Pure ALOHA protocol
    Slotted ALOHA protocol

## Slide 12: Pure ALOHA
Let users transmit whenever they have data to be sent.
There will be collisions, of course, and the colliding frames will be damaged. Senders need some way to find out if this is the case.
After each station has sent its frame to the central computer, this computer rebroadcasts the frame to all of the stations.
A sending station can thus listen for the broadcast from the hub to see if its frame has gotten through.
If the frame was destroyed, the sender just waits a random amount of time and sends it again.
Systems in which multiple users share a common channel in a way that can lead to conflicts are known as contention systems

## Slide 14: Slotted ALOHA
… proposal was to divide time into discrete intervals called slots, each interval corresponding to one frame
This approach requires the users to agree on slot boundaries.
One way to achieve synchronization would be to have one special station emit a pip at the start of each interval, like a clock.
it is required to wait for the beginning of the next slot

## Slide 16: Carrier Sense Multiple Access Protocols
Carrier Sense Multiple Access Protocols – CSMA
Protocols in which stations listen for a carrier (i.e., a transmission) and act accordingly are called carrier sense protocols

## Slide 17: Carrier Sense Multiple Access Protocols
Carrier Sense Multiple Access Protocols – CSMA
Protocols in which stations listen for a carrier (i.e., a transmission) and act accordingly are called carrier sense protocols
Persistent and Nonpersistent CSMA
Persistent - নাছোড়বান্দাভাবে রত

## Slide 18: 1- Persistent CSMA Protocol

## Slide 19: 1- Persistent CSMA Protocol
When a station has data to send:
  It first listens to the channel to see if anyone else is transmitting at that moment.
  If the channel is idle, the stations sends its data.
  if the channel is busy, … waits until it becomes idle. Then the station transmits a frame
  if a collision … waits a random amount of time and starts all over again.
  The protocol is called 1-persistent because the station transmits with a probability of 1 when it finds the channel idle

## Slide 20: 1- Persistent CSMA Protocol

## Slide 21: Nonpersistent CSMA
A station senses the channel when it wants to send a frame, and if no one else is sending, the station begins doing so itself.
However, if the channel is already in use, the station does not continually sense it for the purpose of seizing it immediately upon detecting the end of the previous transmission.
Instead, it waits a random period of time and then repeats the algorithm.

## Slide 22: P-persistent CSMA
It applies to slotted channels and works as follows.
  When a station becomes ready to send, it senses the channel.
  If it is idle, it transmits with a probability p.
  With a probability q = 1 − p, it defers until the next slot.
  If that slot is also idle, it either transmits or defers again, with probabilities p and q.
  This process is repeated until either the frame has been transmitted or another station has begun transmitting.
  if there had been a collision - it waits a random time and starts again.
  If the station initially senses that the channel is busy, it waits until the next slot and applies the above algorithm.

## Slide 23: CSMA with Collision Detection
CSMA with Collision Detection – CSMA/CD
A
B
C
D

## Slide 24: CSMA with Collision Detection

## Slide 25: Collison Free Protocol
A Bit-Map Protocol

## Slide 26: Collison Free Protocol
Token Passing