## Slide 1
Dr. Asif Zaman
Associate Professor, CSE, RU
CSE3151
Computer Networks
(Session 2018-19)

## Slide 2: Data Link Layer

## Slide 3: Data Link Layer
This actual data is called the payload.

## Slide 5: Data Link Layer
Framing:
  Breaking up the bit stream into frames
Four methods – very popular

## Slide 6: Data Link Layer
Byte Count

## Slide 7: Data Link Layer
Flag Byte with Byte Stuffing
Two consecutive flag bytes indicate the end of one frame and the start of the next.

## Slide 8: Data Link Layer
It may happen that the flag byte occurs in the data, especially when binary data such as photographs or songs are being transmitted. This situation would interfere with the framing.
One way to solve this problem is to have the sender’s data link layer insert a special escape byte (ESC) just before each ‘‘accidental’’ flag byte in the data. This technique is called byte stuffing

## Slide 10: Data Link Layer
Flag bits with bit stuffing
Each frame begins and ends with a special bit pattern, 01111110 or 0x7E in hexadecimal.

## Slide 11: Data Link Layer

## Slide 12: Data Link Layer
Types of Errors
  Errors can be of three types, namely
    single bit errors,
    multiple bit errors, and
    burst errors.

## Slide 13: Data Link Layer

## Slide 14: Data Link Layer
Error
  error-correcting codes and
  error-detecting code
Popular error-correcting codes:

## Slide 15: Data Link Layer
Hamming Code
  A frame consists of data (i.e., message) bits and
  redundant (i.e. check) bits.
Suppose the number of data bits is 7, then the number of redundant bits can be calculated using: = Thus, the number of redundant bits= 4

## Slide 16: Hamming Code
Parity bits –
  A parity bit is a bit appended to a data of binary bits to ensure that the total number of 1’s in the data are even or odd. Parity bits are used for error detection.
  There are two types of parity bits:
    Odd parity
    Even Parity

## Slide 17: Hamming Code
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
D11 | D10 | D9 | R8 | D7 | D6 | D5 | R4 | D3 | R2 | R1
1011001
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | R2 | R1

## Slide 18
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | R2 | R1
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1

## Slide 19: Hamming Code
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | R2 | R1

## Slide 20
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | R2 | R1
Even Parity:
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | 1 | 0
1 | 0 | 1 | R8 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | R8 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | R2 | 0
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | R2 | 0
1 | 0 | 1 | R8 | 1 | 0 | 0 | R4 | 1 | 1 | 0
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1

## Slide 21
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
0
Sender
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
https://www.geeksforgeeks.org/hamming-code-in-computer-network/

## Slide 22: Error Detection
Error Detection

## Slide 23: Error Detection
Simple Parity Check

## Slide 24: Error Detection
Two Dimensional Parity Check

## Slide 25: Error Detection
Checksum:
https://www.geeksforgeeks.org/error-detection-in-computer-networks/

## Slide 26: Error Detection
CRC:
https://www.geeksforgeeks.org/error-detection-in-computer-networks/